## Slide 1: Presentation – RISCV CPU
杨宗翰 2020.1.4

## Slide 2: Introduction
My CPU is a standard 5 stage pipeline CPU.
So what is my point of this presentation?
My understand of circuits, and
How to achieve high frequency on FPGA?
And the problems I found.

## Slide 3: Some jokes

## Slide 4: Circuits
Sequential Circuit
Combinational Circuit

## Slide 5: Sequential Circuit
Action at the specific signal.
All results of all cases calculated parallelly.
All data used ‘as is’ at the instant of signal occurs.
It will choose answers by cases.
Latency is calculated as maximum case sequences latency or the maximum calculation latency.
Critical path: Memory Controller

## Slide 6: Combinational Circuit
Action at the input changes.
For a register that we change, it
  Clear data in it
  Receive new assignment
So every register we change in the combinational circuits CAN’T be a condition or don’t change in some paths, or it will lead to a latch.
Latency is calculated as the maximum calculation sequences latency.
Critical path: ID – REGFILE – ID, IF – CACHE – IF

## Slide 7: How to achieve a good frequency？
Good frequency = Low latency
A good design is required!

## Slide 8: Where are bottlenecks？
IF
ICACHE
ID
EX
MEM
REGFILE
MEMCTRL
SCACHE
IF/ID
ID/EX
EX/MEM
MEM/WB
STALLBUS
PC_REG
Data Forwarding
Branch
Data
Stall Enable
Stall Request
RAM/HCI
PREDICTOR
Branch Prediction

## Slide 9: Where are bottlenecks？
IF
ICACHE
ID
EX
MEM
REGFILE
MEMCTRL
SCACHE
IF/ID
ID/EX
EX/MEM
MEM/WB
STALLBUS
PC_REG
RAM/HCI
PREDICTOR

## Slide 10: Bottlenecks
ID is slow
  ID needs 2 levels of combinational circuits and 2 levels of big cases.
  Data requirements are slow!
    Generally, it will need 2 combinational circuits action at the same time.
Caches are slow
  Tag comparation plus RAM addressing is slow
  Caches are giant, so the path latency is large.
  If implement cache with combinational circuits, there will be 2 levels of slow combinational circuits.
Memory controller is slow
  Very complex sequential circuit
EX can be slow – if use a big case

## Slide 11: Some solutions
EX branch
  Improve ID performance
  With predictor it’s not slow; without predictor JAL can jump at ID.
Sequential cache refresh
  Late one cycle improves much on performance
Sequential predictor refresh
Size – latency balanced cache/predictor size
Clear memory controller design
Modularization design of EX
  Use parallelism

## Slide 12: Module design of EX
Titan ALU
Small ALU
Small ALU
Small ALU
Small ALU
MUX
Much more latency
Lower latency

## Slide 13: My other features
Cache
  1KiB Direct Mapped Instruction Cache
  128B Direct Mapped Stack Cache
  Why Direct Map?
    2:1 Cache rule
    Lower latency.
    I implemented 2-way associative cache, it works worse.
4 cycle instruction fetch (prefetch)
Branch Prediction: 128 lines of BTB

## Slide 14: My result
Achieved 210MHz.
Running pi.c @210 MHz using s.
Running stress test @200 MHz using s.
  Stress test is a test that provided by 于峥
  Very many (about) instructions
Running gcd.c @iVerilog using ns.

## Slide 15: My problems met during implementation
Just some jokes about me.
  Implemented BGE with >.
  When both stalled and jumped, IF/ID and ID/EX clears wrongly.
    I create a test to infer this problem
  The first version failed on FPGA, because MEM latched so much that I can't fix.
  When I tried to find a way to fetch in 4 cycles, I failed with 7, 8, or even 10 cycles.
  assign rst = rst_in | (~rdy_in);
  ram_data_o <= {24'h0,sdata[ram_addr_i[``SCacheIndex] + 1],sdata[ram_addr_i[``SCacheIndex]]};

## Slide 16: Problems in riscv_top.v
posedge 0:
  MCTL send a request in order to access RAM or I/O.
posedge of cycle 1:
  TOP access RAM or HCI by the higher 2 bits of address.
posedge of cycle 2:
  TOP return the data by the type REQUESTED IN CYCLE 1(should be 0)
Cause:
assign hci_io_en = (cpumc_a[RAM_ADDR_WIDTH:RAM_ADDR_WIDTH-1] == 2'b11) ? 1'b1 : 1'b0;
Solution
  Use sequential circuits to refresh hci_io_en.

## Slide 17: Problems in pi.c
WRONG ANSWER
314159265358979323846264338327950288…
The original program uses %04d.
But our source uses outl().
That is different.

## Slide 18: Problems in UART buffer
Buffer size is too small.
I didn’t read the code but as it’s commented in C source, the improvement was not introduced in UART codes.
Question: Is SLEEP the best way to prevent HW drawback?

## Slide 19: Some jokes

## Slide 20: Questions?
Any questions is welcomed!

## Slide 21: Thank you!
杨宗翰 2020.1.4
And thank you: (in no particular order)
李照宇
张志成
于峥
庄永昊
陈伟哲
姚远
雷思磊（Author of ‘自己动手抄写 CPU’）
And everyone who discussed with me and inspired me
… but the space is too small to mention.